## Slide 1: Neutron Diffusion in Weapons
Historical
Notes
Spherical
Basics
Cartesian
Cylindrical
18/07/2022
1

## Slide 2: History of Nuclear Weapons
How Manhattan Project produced the first atomic bomb
1939
Start of the Project
A letter outlining concerns that Germany may be developing nuclear bomb technology causes the creation of Manhattan Project
1942
New Director
J. Robert Oppenheimer, becomes the director of the Los Alamos National Laboratory
1945
July
Trinity
There is the first nuclear explosion, Trinity
1945
9 August
Little Boy, Fat Man
Fat Man and Little Boy are dropped on Hiroshima and Nagasaki
1945
15 August
Japan Surrenders
After the Soviet Union’s declaration of war and the bombing, Japan surrenders
2022
Xotta Francesco
02
Notes: 2

## Slide 3: Conditions of this Work:
Dirichlet Boundary Conditions
Parameters taken from the following table
Graham W. Griffiths
18/07/2022
Xotta Francesco
3

## Slide 4: Critical Mass:
The equation for the diffusion of neutron is
With initial and boundary conditions
Where:
n is the neutron density
µ is the diffusion constant (µ = λt vneut /3)
η is the neutron rate of formation (η = vneut(ν − 1)/λf)

## Slide 5: 1-D Example:
In one dimension we solve for n(t, x) = T(t)X(x), so that
Dividing it by TX and rearranging:
We have thus two ODEs to solve, with general solutions

## Slide 6: 1-D Example:
We now express n using the superposition principle as
Where we need to have
For n to grow unbounded (critical condition) we need to have
And, using that p=1 is the worst case, L=11.04 cm.

## Slide 7: Numerical Solution:
We will need to:
Include Libraries:
#include <iostream>
#include <cmath>
#include <math.h>
#include <fstream>
#include "Numerics.h"
Define functions and global variables:
double L,A,lambda,mu,eta;
int N;
int p=0;
double Function (double x)
{
return A*exp( -lambda*(pow(((x-L/2)/(L/2)),2) ));
};
double Int (double x)
{
return 2*Function(x)*sin(p*M_PI*x/L)/L;
}
Read Input:
fstream newfile;
newfile.open("config.txt",ios::in);
if (newfile.is_open())
{
newfile >> L >> A >> lambda >> N >> mu >> eta; //0.111 1 100 31 2.3446e+05 1.8958e+8 are the suggested values
} else
{
exit(EXIT_FAILURE);
}
newfile.close(); //close the file object.

## Slide 8: 1-D Example: Coefficients
We need to compute the coefficients a, given by the equation
And for this we develop the following code:
double Numerics::trapezoidal(double (*f)(double), double a, double b, double h)
{
/**Integral solver that uses the trapezoidal method; it solves between a and b with step distance h*/
int Nstep=abs((b-a)/h);
double Area=0;
for (int i=0;i<Nstep;++i){
Area=Area+(f(a+(i+1)*h)-f(a+i*h))*h/2+f(a+i*h)*h;
}
return Area;
};
double *a=new double[N];
Numerics num;
double n;
for (p=0;p<N;++p)
{
a[p]=num.trapezoidal(Int,0,L,0.0001);
cout << a[p] << " ";
}

## Slide 9: 1-D Example: Functions
Where
double Function (double x)
{
return A*exp( -lambda*(pow(((x-L/2)/(L/2)),2) ));
};
double Int (double x)
{
return 2*Function(x)*sin(p*M_PI*x/L)/L;
}

## Slide 10: 1-D Example: Neutron Density
int NPoints=abs(L/dx);
int NStep=abs(tfin/dt);
newfile.open("output.txt",ios::out);
newfile << "n(x,t)" << " " << "t" << " " << "x" << endl;
for (int c=1; c<NStep; ++c)
{
for (int i=1; i<NPoints; ++i)
{
n=0;
for (p=1;p<N;++p)
{
n=n+a[p]*exp(eta*(c*dt)-mu*(p*M_PI/L)*(p*M_PI/L)*(c*dt))*sin(p*M_PI*i*dx/L);
}
newfile << n << " " << c*dt << " " << 0+i*dx << endl;
};
};
Matlab Script:
data = readtable('output.txt’);
A=table2array(data(:,1:3));
plot3(A(:,3),A(:,2),A(:,1));

## Slide 11: Cartesian 3D:
We can extend the previous derivation to multiple dimensions; for three dimensions
For shortest L (p=q=r=1) we have
Which means for a cubic box

## Slide 12: Cartesian 3D: Coefficients
For the coefficients we compute
With starting condition given by
We need to compute those coefficients numerically

## Slide 13: Cartesian 3D: Functions
We define the following functions:
double Function (double x, double y, double z)
{
return (1 -( x / L ) ) *(1 -( y / L ) ) * (1 -( z / L ) ) * x * y * z /pow(( L /2),3); //The initial condition were different this time
};
double Int (double x, double y, double z) //It's way easier to define the integrand like this
{
return 8*Function(x,y,z)*sin(p*M_PI*x/L)*sin(q*M_PI*y/L)*sin(r*M_PI*z/L)/(L*L*L);
}

## Slide 14: Cartesian 3D: Coefficients
Numerics num;
double n;
for (p=0;p<N;++p)
{
for (q=0; q<N; ++q)
{
for (r=0; r<N; ++r)
{
a[p][q][r]=num.trapezoidal(Int,0,L,0,L,0,L,0.01);
cout << a[p][q][r] << " ";
};
cout << endl;
}
};
double Numerics::trapezoidal(double (*f)(double, double, double), double ax, double bx, double ay, double by, double az, double bz, double h)
{
/**Integral solver that uses the trapezoidal method; it solves between [ax,bx], [ay,by], [az,bz] with step distance h; it solves for z for each step of y, which solves for each step of x*/
int Nstepx=abs((bx-ax)/h);
int Nstepy=abs((by-ay)/h);
int Nstepz=abs((bz-az)/h);
double Area=0;
for (int i=0;i<Nstepx;++i)
for (int c=0; c<Nstepy; ++c)
for (int k=0; k<Nstepz; ++k)
Area=Area+(f(ax+(i+1)*h,ay+(c+1)*h,az+(k+1)*h)-f(ax+i*h,ay+c*h,az+k*h))*h*h*h/2+f(ax+i*h,ay+c*h,az+k*h)*h*h*h;
return Area;
};

## Slide 15: Cartesian 3D: Neutron Density
int NPoints=abs(L/dx); //it's a cubic box L*L*L
newfile.open("output.txt",ios::out);
newfile << "n(" << t <<",x,y,z)" << " " << "x" << " " << "y" << " " << "z" <<endl;
for (int i=1; i<NPoints; ++i)
for (int k=1; k<NPoints; ++k)
for (int l=1; l<NPoints; ++l)
{
n=0; //At the end of every loop in p,q,r, n must be reset
for (p=1;p<N;++p)
for (q=1; q<N;++q)
for (r=1; r<N; ++r)
n=n+a[p][q][r] * exp( eta*(t)-mu*( pow((p*M_PI/L),2)+ //INDENTATION CHANGED FOR PPT
pow((q*M_PI/L),2)+
pow((r*M_PI/L),2) )*(t)) * sin(p*M_PI*i*dx/L) * sin(q*M_PI*k*dx/L) * sin(r*M_PI*l*dx/L);
newfile << n << " " << 0+i*dx << " " << 0+k*dx << " " << 0+l*dx << endl;
};

## Slide 16: Cylindrical 3D:
Given the laplacian in cylindrical coordinates
(where the angular derivative disappears due to radial symmetry) we can write
With n(t, r1, z) = 0, n(t, r, 0) = 0, n(t, r, L) = 0 and n(0, r, z) = f(r, z).
We solve as before (separable variables) and reuse the superposition principle so that:
with J0 being the order 0 Bessel function of first type with being its qth zero.

## Slide 17: Cylindrical 3D:
Notice that for values of p different than 1 the coefficients would be 0; criticality condition will be
Where, assuming p=q=1, we obtain (solving for the radius):
We can then compute the volume V= and differentiate it with respect to L, equating to 0 and obtaining a critical value of
Which we substitute into to obtain the critical radius

## Slide 18: Cylindrical 3D: Coefficientss
We can compute the coefficients with the formula
With initial condition

## Slide 19: Cylindrical 3D: Functions
We define
double Function (double r, double z)
{
return A*(1-pow(r/r1,2))*sin(M_PI*z/L);
};
double Int (double r, double z) //It's way easier to define the integrand like this
{
return 4* Function(r,z)*r* sin(M_PI*z*p/L) * j0(r*alpha[q]/r1) /(L*pow(j1(alpha[q])*r1,2));
}

## Slide 20: Cylindrical 3D: Bessel Functions
We need to define Bessel Functions’ zeros by reading them in an array:
alpha=new double[N];
newfile.open("besselzeros.txt",ios::in);
for (int i=0; i<N; ++i)
{
newfile >> alpha[i];
};
newfile.close();

## Slide 21: Cylindrical 3D: Coefficients
Using p=1 (as we said before):
double* a=new double [N];
Numerics num;
double n;
for (q=0;q<N;++q)
{
a[q]=num.trapezoidal(Int,0,r1,0,L,0.001);
cout << a[q] << " ";
cout << endl;
};
double Numerics::trapezoidal(double (*f)(double, double), double ax, double bx, double ay, double by, double h)
{
/**Integral solver that uses the trapezoidal method; it solves between [ax,bx] and [ay,by] with step distance h; it solves for y for each step of x*/
//We want to integrate by strings, so for constant x we integrate over y
int Nstepx=abs((bx-ax)/h);
int Nstepy=abs((by-ay)/h);
double Area=0;
for (int i=0;i<Nstepx;++i)
for (int c=0; c<Nstepy; ++c)
Area=Area+(f(ax+(i+1)*h,ax+(c+1)*h)-f(ax+i*h,ay+c*h))*h*h/2+f(ax+i*h,ay+c*h)*h*h;
return Area;
};

## Slide 22: Cylindrical 3D: Neutron Density
int NPoints=abs(L/dx);
int NPointsr=abs(r1/dx);
newfile.open("output.txt",ios::out);
newfile << "n(" << t <<",r,z)" << " " << "r" << " " << "z" <<endl;
for (int i=1; i<2*NPointsr; ++i)
for (int k=1; k<NPoints; ++k)
{
n=0; //At the end of every loop in p,q,r, n must be reset
for (q=0;q<N;++q)
n=n+a[q] * j0((-r1+i*dx)*alpha[q]/r1) * sin(p*M_PI*k*dx/L) * exp( t * ((eta*pow(r1*L,2)-mu*( pow(alpha[q]*L,2) + pow(M_PI*p*r1,2) )) )/pow(r1*L,2));
newfile << n << " " << -r1+i*dx << " " << 0+k*dx << endl;
};
newfile.close();

## Slide 23: Spherical 3D:
Let’s now consider a sphere of fissile material, with a laplacian given as
Which is reduced due to radial symmetry to .
So we can write now the neutron diffusion equation
With boundary and initial conditions given as n(t, r1) = 0; n(0, r) = f(r)
Using the previous approach we obtain

## Slide 24: Spherical 3D:
With so that
The critical condition will be
Which gives, for p=1, the critical radius which is 11.04 cm for Uranium-235.
For the coefficients
With

## Slide 25: Spherical 3D: Functions
We define
double Function (double r)
{
return 1-pow(r/r1,2); //
};
double Int (double r) //It's way easier to define the integrand like this
{
return 2*Function(r) *r* sin(p*M_PI*r/r1) / r1; //we get 2 times the results given in the paper, which seems to be wrong
}

## Slide 26: Spherical 3D: Coefficients
double* a=new double [N];
Numerics num;
for (p=0;p<N;++p)
{
a[p]=num.trapezoidal(Int,0,r1,0.01);
cout << a[p] << " ";
cout << endl;
};

## Slide 27: Spherical 3D: Neutron Diffusion
int Nstep=abs(t/dt);
int NPointsr=abs(r1/dx);
newfile.open("output.txt",ios::out);
newfile << "n(t,r)" << " " << "t" << " " << "r" <<endl;
for (int i=1; i<2*NPointsr; ++i)
{
for (int k=1; k<Nstep; ++k)
{
n=0;//At the end of every loop in p,q,r, n must be reset
//if (-r1+i*dx!=0) If we want to avoid infinities in the denominator this is a rather expensive method
{
for (p=1;p<N;++p)
n=n+ (a [ p ]/ (-r1+i*dx) ) * exp ( eta *k*dt - mu *pow((( p ) * M_PI / r1 ),2) *k* dt ) * sin (( p ) * M_PI * (-r1+i*dx) / r1 );
newfile << n << " " << 0+k*dt << " " << -r1+i*dx << endl;
};
};
};

## Slide 28: Brief Summary:
For Dirichlet Boundary condition we can see that
Vsphere : Vcyl : Vcube = 1 : 1.142 : 1.241
How much different would be the critical radius assuming Neumann Boundary Condition?

## Slide 29: Neumann BC:
Let’s assume now that we are still considering a sphere of fissile material with boundary condition
But everything else identical to the spherical case; we can thus use n(t,r)=T(t)R(r) so that
And
Whose solutions are, assuming
and

## Slide 30: Neumann BC:
We then solve for =1 to get the critical radius:
We can do this numerically, defining R as its general solution:
double Rfunc (double r){
return (A*sin(k*r))/r;
};
double Rfuncprime (double r){
Numerics num;
return num.derivative(Rfunc,0.00001,r);
}
double neumannBC(double r)
{
return Rfuncprime(r)+3*Rfunc(r)/(2*lambdat);
};
double Numerics::derivative (double (*func)(double), double dx, double pointx){
/**A simple 5 points formula that gives the derivative of func in pointx using dx as small distance*/
return (func(pointx-2*dx)-8*func(pointx-dx)+8*func(pointx+dx)-func(pointx+2*dx))/(12*dx);
};

## Slide 31: Neumann BC:
We then solve the equation to get r1:
r1=num.bisection(neumannBC,0,10,1e-5);
Obtaining a radius of 8.369 cm.
We can then compute what happens for R>r
double Numerics::bisection(double (*f)(double), double a, double b, double error)
{
/**Simple Root Finding algorythm that uses bisection; it solves between a and b; if f has more than one 0 between a and b it may not give any result*/
double newpar=a+(b-a)/2;
if (b<a)
{
swap(a,b);
}
if (abs(b-a)<abs(error) || abs(f(newpar))==0)
return newpar;
if (f(a)*f(newpar)<=0) //Recursive condition
return bisection(f,a,newpar,error);
else if (f(newpar)*f(b)<=0)
return bisection(f,newpar,b,error);
else
{
cout << "Error: number of zeros in the selection is not 1"<<endl;
return a;
}
};

## Slide 32: Neumann BC:
We define for R=8.5 cm:
double newalpha (double a)
{
return -1 + 3*R/lambdat/2 + R*sqrt((eta+a)/mu)*cos(R*sqrt((eta+a)/mu))/sin(R*sqrt((eta+a)/mu));
};
double alphaprime(double r)
{
Numerics num;
return num.derivative(newalpha, 0.00001, r);
};
So that in the main:
R=8.5;
alpha=num.newton(newalpha,alphaprime, 0, 1e-7,100);
double Numerics::newton(double (*func)(double), double (*funcprime)(double), double p0, double err, int Nloop)
{
/**Simple Root Finding algorythm that uses Newton method; it requires a function func and its derivative funcprime. It also wants a starting point p0*/
double p=p0-func(p0)/funcprime(p0);
if (Nloop==0)
{
cout <<"There is no 0 that could be found in the suggested number of loops"<<endl;
return p0;
};
if ((func(p) == 0) || (abs(p-p0) < err))
return p;
else
return newton(func,funcprime,p,err,Nloop-1);
};

## Slide 33: Neumann BC: Neutron Diffusion
The initial conditions don’t need to be too precise, so we can just set n=1 at the surface (n(t=0,r=8.5)=1), then we compute n:
int NPoints=2*abs(R/dx);
int NStep=abs(tfin/dt);
A=1/ (sin ( k * R ) / R);
cout <<k<< " "<<alpha<< " "<<R<<" "<< A << endl;
newfile.open("output.txt",ios::out);
newfile << "n(r,t)" << " " << "t" << " " << "r" << endl;
for (int c=1; c<NStep; ++c)
{
for (int i=1; i<NPoints; ++i)
{
n=A*exp(- alpha *c*dt)*sin(k*(-R+i*dx))/(-R+i*dx);
newfile << n << " " << c*dt << " " << -R+i*dx << endl;
};
};

## Slide 34: Tamper
Since fissile material is expensive we need to use it efficiently!
We surround the fissile material with a reflector material (generally heavy elements) that can reflect escaping neutrons back inside.
This is called a ‘tamper’ or ‘containment shell’
It also prevents the fissile material from increasing too much in size, avoiding the premature end of the chain reaction.

## Slide 35: Mean Free Path:
Consider a slab of:
thickness s,
cross sectional-area Σ
Bombarded by neutrons at a rate of R0 neutrons per square meter per second
The number density of nuclei in the slab is
V=Σs ⇒ Nnuclei=Σsn ⇒ A= Σsnσ ⇒ R = (R0Σ) snσ
Prx= snσ = probability of a reaction
Pesc=1- Prx= 1-snσ = Probability of a neutron escaping
Given N0 the number of incident neutrons then, given m slabs of thickness s: where z= -sn, x=s*m

## Slide 36: Mean Free Path:
We rewrite (where the last equality is true for very small s).
from which =probability of a single neutron initiating a reaction
Density function:
Expectation Value: which reduces to for large L.

## Slide 37: Mean Free Path: Numerics
We use a script to compute the probability and number of neutron reacting or escaping:
cout << "How thick will the slab be?"<<endl<<"x: ";
cin>>x;
cout << endl;
Nesc=N0*pow(Pesc, x/s);
z=s*n*sigma;
cout << Nesc<<" ";
Nesc=N0*pow(1+z,-sigma*n*x/z); //Nesc=N0*pow(pow(1+z,1/z),-sigma*n*x);
cout << Nesc << " "<<endl;
Nesc=N0*exp(-sigma*n*x);
Nreact=N0-Nesc;
cout << "The number of reactions is: "<< Nreact << endl;
And we compare the different formulas derived above

## Slide 38: Mean Free Path: Numerics
We then plot the probability density and derive the mean free path:
int NStep=abs(x/dx);
xm=num.integration(Int,0,x,1e-3);
cout<<"The expectation value is: "<<xm<<endl;
for (int c=1; c<NStep; ++c)
{
newfile << prx(c*dx) <<" "<< c*dx<<endl;
};
We find then that the mean free path is 16.89 cm